## Slide 1
Cisco C9200CX-12P-2X2G-E
vs. Cisco IE-3500H-12P2MU2XE
Enterprise Compact Access vs. Industrial Heavy-Duty Ethernet
Context: Same-format validated comparison for harsh-environment deployment decisions
Prepared For: Carnival
Validated against official Cisco datasheets and installation guides
March 2026

## Slide 2
Executive Summary
IE-3500H-12P2MU2XE is an industrial near-match, not a 1:1 enterprise peer
Metric | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Design Intent | Enterprise compact access | Industrial / heavy-duty Ethernet
Ports | 12x 1G PoE+ + 2x 10G SFP+ | 12x M12 1G PoE + 2x 10G/1G SFP + 2x mGig/4PPoE
Power Input | 100-240V AC internal | 12-54V DC industrial
Ingress Protection | No IP rating | IP66/IP67
Operating Temp | -5°C to 45°C | -40°C to 75°C
PoE Budget | 240W | 240W
MACsec | AES-256 | MACsec-128 on -E license
Stacking | Not supported | Not supported
Weight | 6.6 lb (2.99 kg) | 11.40 lb (5.17 kg)
▶ C9200CX is lighter and campus-oriented; IE3500H is heavier but purpose-built for harsh environments.
▶ If the real requirement is industrial sealing, DC power, M12, and vibration hardening, IE3500H is the correct class of product.
Carnival | C9200CX vs IE3500H | Slide 2 of 14
Validated March 2026

## Slide 3
Fit Assessment: Is IE-3500H-12P2MU2XE the Closest Match?
Validated interpretation of the user-provided candidate
Question | Answer | Impact
Is it a 12-port PoE Cisco alternative? | Yes, partially | It matches the 12-port PoE requirement but adds extra industrial ports.
Is it a direct port-for-port peer? | No | IE3500H has 2 extra mGig/4PPoE ports and M12 industrial connectors.
Is it closer in environment / ruggedness? | Yes | It is the correct Cisco family if harsh-environment deployment is the real requirement.
Is it closer in enterprise access behavior? | No | The C9200CX remains the cleaner fit for standard campus/branch access switching.
▶ This comparison is valid for decision-making, but it compares an enterprise compact switch to an industrial heavy-duty switch.
▶ The deck explicitly treats IE3500H as a harsh-environment near-match, not a strict 1:1 replacement.
Carnival | C9200CX vs IE3500H | Slide 3 of 14
Validated March 2026

## Slide 4
Ports, Uplinks, and Physical Interfaces
Parameter | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Primary PoE Ports | 12x 10/100/1000 RJ-45 PoE+ | 12x 10/100/1000 M12 X-code PoE
Uplink Ports | 2x 10G SFP+ | 2x 10G/1G SFP
Additional Ports | None | 2x mGig / 4PPoE industrial ports
Management / Console | RJ45 + USB console / USB-A | M12 A-coded 5-pin console
Connector Standard | Enterprise RJ-45 | Industrial M12
Total Port Count | 14 logical external interfaces | 16 total interfaces
▶ IE3500H is not just a rugged C9200CX: it changes the physical interface model with M12 and extra industrial ports.
▶ If field cabling already uses M12 or requires sealed connectors, IE3500H has a major deployment advantage.
Carnival | C9200CX vs IE3500H | Slide 4 of 14
Validated March 2026

## Slide 5
PoE, Power Architecture, and 4PPoE
Parameter | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
PoE Standard | IEEE 802.3at PoE+ (30W/port) | IEEE 802.3at PoE+ + industrial 4PPoE-capable ports
PoE Budget | 240W | 240W
Max Port Power | 30W | Up to 90W on 4PPoE-capable ports
Input Power | 100-240V AC | 12-54V DC
Max System Draw | 315W AC internal PSU | 45W base system without PoE (Cisco published)
Deployment Bias | Enterprise wiring closets | Industrial DC / OT power environments
▶ Both switches offer 240W PoE budget, but IE3500H aligns better with DC-powered industrial infrastructure.
▶ If the use case needs 4PPoE / high-power industrial endpoints, IE3500H expands beyond standard PoE+.
Carnival | C9200CX vs IE3500H | Slide 5 of 14
Validated March 2026

## Slide 6
Performance, Scale, and Memory
Parameter | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Switching Capacity | 68 Gbps | Not officially published for this SKU
Forwarding Rate | 50.59 Mpps | Line rate for all ports / packet sizes
MAC Address Table | 32,000 | 24,000
VLAN IDs | 4,094 / 4,096 class | 4,096
DRAM | Not officially published per reviewed source set | 8 GB
Flash / User Storage | Not officially published per reviewed source set | 5.1 GB user accessible
IPv4 Routes | Approx. 3,000 class (license/template dependent) | 7,000 IPv4
▶ C9200CX leads in L2 MAC scale; IE3500H leads in published industrial routing scale and memory footprint.
▶ Cisco does not publish every compact C9200CX memory detail cleanly for this exact SKU, so the deck marks those as not officially substantiated.
Carnival | C9200CX vs IE3500H | Slide 6 of 14
Validated March 2026

## Slide 7
Security and Encryption
Feature | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
MACsec | AES-256 on C9200CX | MACsec-128 on Network Essentials (-E)
Secure Boot / Trust Anchor | Yes | Yes
802.1X | Yes | Yes
ACLs | Yes | Yes
Campus Security Features | Stronger campus/security fabric orientation | Industrial security focus rather than campus fabric
SD-Access / DNA Center | Supported | Supported with DNA Center
▶ C9200CX has the cleaner encryption advantage because AES-256 MACsec is standard for the reviewed compact model.
▶ The IE model in the user table ends with -E, so MACsec-256 should not be claimed unless the license changes to Network Advantage.
Carnival | C9200CX vs IE3500H | Slide 7 of 14
Validated March 2026

## Slide 8
L2 / L3 Protocols and Timing
Feature | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Layer 2 | VLANs, STP, RSTP, MST, LACP | VLANs, STP, RSTP, MST, LACP
Static Routing | Yes | Yes
OSPF | Yes (license dependent) | Yes
EIGRP | Yes (license dependent) | Yes
BGP | Limited / platform-license dependent | Supported in reviewed IE3500H source set
PTP (IEEE 1588v2) | Yes | Yes
Industrial Protocols | No | EtherNet/IP, PROFINET, MODBUS / SCADA class support
Redundancy Protocol Bias | Campus bridging/routing | Industrial ring / OT redundancy focus
▶ Both platforms support mainstream L2/L3 and PTP, but IE3500H adds industrial protocol relevance that the campus Catalyst line does not target.
▶ For OT synchronization and industrial interoperability, IE3500H is the more natural fit.
Carnival | C9200CX vs IE3500H | Slide 8 of 14
Validated March 2026

## Slide 9
Environmental Hardening and Industrial Suitability
Criterion | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Ingress Protection | No IP rating | IP66 / IP67
Operating Temperature | -5°C to 45°C | -40°C to 75°C
Shock / Vibration | Not industrial rated | IEC 60068 industrial shock / vibration tested
Salt Mist / Corrosion | Not positioned for marine/industrial exposure | Salt mist testing cited as in progress in reviewed source
Mounting Style | Enterprise compact / cabinet | Industrial wall mount / field deployment
Power Environment | AC-only | DC-ready industrial
▶ IE3500H is the only model in this comparison truly designed for harsh-environment deployment.
▶ If the deployment is marine, outdoor, rail, utility, or factory-like, C9200CX is the wrong product class.
Carnival | C9200CX vs IE3500H | Slide 9 of 14
Validated March 2026

## Slide 10
Industrial Certifications and Deployment Readiness
Certification / Readiness Item | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
IEC / UL Safety | Enterprise safety certifications | Industrial safety certifications
IEEE 1613 / Utility Class | No | Family support / in-progress references depending document
EN50155 / Rail | No | Yes
E-Mark / Automotive | No | Yes
ATEX / IECEx / Harsh OT Positioning | No industrial positioning | Industrial / heavy-duty positioning
Marine Deployment Readiness | Not suitable without major enclosure adaptation | Much closer fit for marine/harsh field scenarios
▶ IE3500H carries the regulatory and environmental posture expected from an industrial Ethernet switch.
▶ C9200CX remains an enterprise compact switch even when its port count looks superficially similar.
Carnival | C9200CX vs IE3500H | Slide 10 of 14
Validated March 2026

## Slide 11
Weight, Dimensions, and Physical Trade-Offs
Parameter | C9200CX-12P-2X2G-E | IE-3500H-12P2MU2XE
Weight | 6.6 lb (2.99 kg) | 11.40 lb (5.17 kg)
Dimensions | 4.4 x 26.9 x 24.4 cm | 26.57 x 27.69 x 8.53 cm
Noise | Fanless / silent | Fanless
Cabinet Impact | Lower weight, easier retrofits | Heavier but more rugged package
Connector Robustness | RJ-45 vulnerable in harsh field use | M12 improves field durability
▶ C9200CX clearly wins on weight and conventional cabinet integration.
▶ IE3500H accepts a weight penalty in exchange for sealed construction and field-grade connector durability.
Carnival | C9200CX vs IE3500H | Slide 11 of 14
Validated March 2026

## Slide 12
Critical Differences from the User-Provided Table
Corrections applied before generating this deck
User Table Claim | Verdict | Correction
C9200CX switching capacity = 128 Gbps | False / contradicted | Use 68 Gbps for this compact SKU; 128 Gbps is not the correct figure for this model.
IE-3500H-12P2MU2XE = 12 ports total | False | It includes 12 main M12 PoE ports plus 2 SFP uplinks and 2 additional mGig/4PPoE interfaces.
IE -E license has AES-256 MACsec | Misleading | For the -E (Network Essentials) variant, reviewed evidence supports MACsec-128, not MACsec-256.
C9200CX and IE3500H are direct peers | Oversimplified | They overlap in PoE compact switching, but one is enterprise access and the other is heavy-duty industrial Ethernet.
▶ The biggest factual fixes are the C9200CX switching-capacity number and the IE3500H total-interface count.
▶ The licensing detail matters: MACsec-256 should not be attributed to the IE -E variant without Network Advantage.
Carnival | C9200CX vs IE3500H | Slide 12 of 14
Validated March 2026

## Slide 13
Recommendation Matrix
Scenario | Recommended Model | Why
Standard enterprise branch / cabin / office access | C9200CX-12P-2X2G-E | Lighter, simpler, AC powered, enterprise access feature set.
Harsh environment / marine exterior / industrial zone | IE-3500H-12P2MU2XE | IP67, M12, DC power, shock/vibration hardening, industrial certifications.
Need conventional RJ-45 access and low weight | C9200CX-12P-2X2G-E | Best fit for standard IT infrastructure.
Need M12 connectors and sealed enclosure | IE-3500H-12P2MU2XE | This is the core reason to choose the industrial platform.
Need strongest MACsec posture on the compared SKUs | C9200CX-12P-2X2G-E | Reviewed configuration has native AES-256 vs IE -E MACsec-128.
Need OT / industrial protocol alignment | IE-3500H-12P2MU2XE | Industrial Ethernet protocols and field deployment posture make it the right class of product.
▶ Choose C9200CX when the environment is enterprise IT; choose IE3500H when the environment itself is the primary constraint.
▶ This is less about raw port counts and more about deployment physics: AC vs DC, RJ-45 vs M12, office vs harsh field.
Carnival | C9200CX vs IE3500H | Slide 13 of 14
Validated March 2026

## Slide 14
Sources & Methodology
Cisco Catalyst 9200 Series Data Sheet
cisco.com/c/en/us/products/collateral/switches/catalyst-9200-series-switches/nb-06-cat9200-ser-data-sheet-cte-en.html
Cisco IE3500 Heavy Duty Series Data Sheet
cisco.com/c/en/us/products/collateral/networking/industrial-switches/ie3500-heavy-duty-series/ie3500-heavy-duty-series-ds.html
Cisco IE3500 Rugged Series Data Sheet
cisco.com/c/en/us/products/collateral/networking/industrial-switches/ie3500-rugged-series/ie3500-rugged-series-ds.html
Cisco IE3500 Hardware Installation Guide
cisco.com/c/en/us/td/docs/IIOT/switches/ie35xx/hw-install-guide/b-ie35xx-hig
Cisco C9200CX Hardware Install Guide
cisco.com/c/en/us/td/docs/switches/lan/catalyst9200/hardware/install/b-c9200cx-hig
Methodology
This deck uses the same validated format as the prior C9200CX replacement presentation. The user-provided comparison table was treated as input only, then corrected against official Cisco datasheets and installation guides. Unsupported values were either removed or labeled as not officially substantiated. IE-3500H-12P2MU2XE is treated as an industrial near-match rather than a strict 1:1 peer.
Carnival | C9200CX vs IE3500H | Slide 14 of 14
Validated March 2026