## Slide 1
Validated Replacement Analysis
Cisco C9200CX-12P-2X2G-E vs Aruba CX 6100 (JL679A) vs Aruba CX 6000 (R8N89A)
Professional fact-check based on vendor sources reviewed on 2026-03-24.
Scope: shipboard deployment considerations, weight, PoE, uplinks, operations, and risk caveats.
Key outcome
Original deck contains multiple material errors
Cisco C9200CX compact model does not support StackWise stacking.
Aruba CX 6100 does support VSF stacking per HPE product information.
Aruba CX 6000 remains 1G-uplink only on the selected model.
Only Cisco provides officially stated 240W PoE on this compact model and AES-256 MACsec in the reviewed sources.
Validated comparison | 1

## Slide 2
Executive summary
Corrected headline findings from official Cisco and HPE Aruba pages/datasheets reviewed.
If 10G uplinks and low weight are required, Aruba CX 6100 is the closest Aruba fit.
If higher PoE headroom, dynamic L3 features, or MACsec are required, Cisco remains stronger.
If management-plane consolidation is important, Aruba CX 6100 gains an advantage because HPE states 8-member VSF support.
If the environment requires marine certification, none of the reviewed vendor sources showed IEC 60945 / DNV certification for these models.
Best Aruba replacement
Aruba CX 6100 JL679A
for 10G uplinks + lower weight
Best capability
Cisco C9200CX
for PoE / MACsec / richer L3
Best caveat
No model is proven marine-certified
in reviewed vendor material
Validated comparison | 2

## Slide 3
Validated specification snapshot
Only values supported by reviewed official product pages / vendor datasheets are shown here.
Metric | Cisco C9200CX-12P-2X2G-E | Aruba CX 6100 JL679A | Aruba CX 6000 R8N89A
Weight | 6.6 lb (2.99 kg) | 6.13 lb (2.78 kg) | 6.17 lb (2.80 kg)
Downlinks | 12x 1G PoE+ | 12x 1G Class 4 PoE | 12x 1G Class 4 PoE
Uplinks | 2x 10G SFP+ + 2x 1G copper | 2x 1/10GbE SFP+ + 2x 1G copper | 2x 1G SFP + 2x 1G copper
PoE budget | 240W | 139W | 139W
Switching capacity | 68 Gbps | 68 Gbps | 32 Gbps
Forwarding rate | 50.59 Mpps | 45.1 Mpps | 23.8 Mpps
Software family | Cisco IOS XE | AOS-CX | AOS-CX
Cooling | Fanless | Fanless 12-port model | Fanless 12-port model
Validated comparison | 3

## Slide 4
What in the original deck was not true
Material corrections that change the recommendation narrative.
Original claim | Status | Correction
Cisco C9200CX provides StackWise stacking | False | Cisco 9200 datasheet explicitly states stacking is not available on C9200CX switches.
Aruba CX 6100 has no stacking | False | HPE store page states 8-member VSF stacking for CX 6100 series.
Aruba CX 6000/6100 both lack stacking | Partly false | Confirmed false for CX 6100; not confirmed for R8N89A in reviewed HPE material.
CX 6000 has 6.13 lb weight | False | Reviewed parsed deck also used 6.17 lb elsewhere; final deck uses 6.17 lb for R8N89A.
Competitive slide claims should be treated as facts | Misleading | Cisco competitive positioning slides are marketing, not neutral proof; keep them separate from validated specifications.
Validated comparison | 4

## Slide 5
Operational and protocol comparison
Kept intentionally conservative: only items supported in reviewed vendor material or clearly caveated.
Criterion | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
Layer role | Layer 3 capable compact access switch | Entry-level Layer 2 with static routing | Entry-level Layer 2 with static routing
Dynamic routing | OSPF / EIGRP / IS-IS / RIP listed in Cisco 9200 datasheet family | Not shown in reviewed HPE product page; positioning is entry-level L2 + static routing | Not shown in reviewed HPE product page; positioning is entry-level L2 + static routing
Telemetry | NETCONF / RESTCONF / YANG / streaming telemetry in 9200 family datasheet | REST API, CLI, Aruba Central, sFlow shown in HPE material | REST API, CLI, Aruba Central, sFlow shown in HPE material
Data-plane encryption | AES-256 MACsec stated for C9200CX models | Not shown in reviewed HPE material | Not shown in reviewed HPE material
Stacking / virtualization | No stacking on C9200CX | 8-member VSF stated by HPE | No reviewed proof of VSF for selected model
PoE per port | Up to 30W PoE+, and 60W applies to 9200CX mGig/UPOE models, not this 12P model | Up to 30W Class 4 PoE | Up to 30W Class 4 PoE
Validated comparison | 5

## Slide 6
Marine-environment decision points
Important criteria missing or weakly supported in the original deck.
Marine certification: none of the reviewed Cisco/HPE sources showed IEC 60945, DNV, or similar marine certification for these exact models.
Salt fog / corrosion: no reviewed vendor source exposed salt-spray compliance for these exact models. Treat as open risk until vendor confirms.
Shock / vibration: no reviewed official source exposed marine shock/vibration compliance for these exact models.
Operating temperature: Cisco reviewed source shows -5 to 45°C for C9200CX; Aruba reviewed sources position the products as commercial campus/branch access switches.
MTBF: Cisco family documentation contains MTBF sections; Aruba public product pages reviewed here did not give an MTBF value for the selected models.
Stacking impact at 2,000-2,500 units per ship: Aruba CX 6100 VSF can reduce management objects; Cisco compact model cannot stack.
Procurement note: if marine compliance is mandatory, request written vendor evidence for vibration, corrosion, humidity, MTBF, and coating before final selection.
Validated comparison | 6

## Slide 7
Recommendation matrix
Neutral recommendation after correcting unsupported claims.
Scenario | Recommended model | Why
Need 10G uplinks and lowest practical Aruba replacement weight | Aruba CX 6100 JL679A | Keeps 10G-capable uplinks and lowers weight vs Cisco.
Need higher PoE budget or richer campus feature set | Cisco C9200CX-12P-2X2G-E | 240W PoE, Cisco 9200 family programmability, and reviewed MACsec support.
Need 1G-only access with lowest cost among compared models | Aruba CX 6000 R8N89A | Viable only if 1G uplinks and simpler L2/static-routing profile are acceptable.
Need management-plane consolidation across many edge switches | Aruba CX 6100 JL679A | Reviewed HPE material states 8-member VSF support; Cisco compact model does not stack.
Need marine-certified platform | No validated winner | None of the reviewed sources proved marine certification for these exact switches.
Validated comparison | 7

## Slide 8
Primary sources reviewed
Use these links as the evidence set behind the corrected deck.
Cisco Catalyst 9200 Series Data Sheet: cisco.com/.../nb-06-cat9200-ser-data-sheet-cte-en.html
HPE Store — Aruba CX 6100 JL679A product page: buy.hpe.com/.../jl679a
HPE Store — Aruba CX 6000 R8N89A product page: buy.hpe.com/.../r8n89a
HPE Aruba Networking CX 6100 Switch Series data sheet: hpe.com/psnow/doc/a00106853enw
HPE Aruba Networking CX 6000 Switch Series data sheet: hpe.com/psnow/doc/a00112996enw
Methodology: unsupported marketing claims and community opinions were excluded from the final recommendation unless backed by vendor material. Where evidence was incomplete, the slide deck now says “not validated” instead of guessing.
Validated comparison | 8