## Slide 1
Competitive Overview
C9200CX Competitive Comparison
Expanded master deck including Aruba, Arista, IE3500 Rugged, and IE3500H
Prepared for: Carnival
March 2026
• Expanded from the validated Aruba, Arista, IE3500H, and official IE3500 Rugged fact set.
• Keeps C9200CX as the reference in all categories.
• Uses the same Cisco-style format as the prior master deck, but now includes IE3500 Rugged Series.
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
1

## Slide 2
Key Technical Findings:
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
2
• C9200CX remains the best all-around campus access platform when PoE headroom, MACsec-256, telemetry, visibility, and Cisco campus integration matter most.
• Arista CCS-710P-12 is the closest true compact near-match, with very similar physical role and lower switching power draw.
• Aruba CX 6100 wins the weight and stacking category, but it trades away major security, telemetry, and PoE headroom.
• IE3500 Rugged Series and IE3500H Heavy Duty split the industrial category: Rugged wins modular DIN-rail / RJ45 flexibility, while IE3500H wins sealed IP66/IP67 harsh-environment deployment.

## Slide 3
Cisco Catalyst 9200CX Switches
Competitive Landscape
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
3
Platform | Compared Model / Series | Role | Primary Win
Cisco | C9200CX-12P-2X2G-E | Reference compact campus switch | 🏆 All-around campus feature depth
Aruba | CX 6100 (JL679A) | 10G-capable Aruba compact alternative | Weight / VSF stacking
Aruba | CX 6000 (R8N89A) | Lower-end 1G-uplink option | Basic access only
Arista | CCS-710P-12 | Closest compact near-1:1 match | Closest clean hardware substitute
Cisco Industrial | IE3500 Rugged Series | DIN-rail modular industrial family | RJ45 / modular / dual-DC industrial flexibility
Cisco Industrial | IE-3500H-12P2MU2XE | Heavy-duty sealed industrial near-match | Rugged / IP67 / DC / M12

## Slide 4
Executive Summary
Multi-vendor validated snapshot
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
4
Metric | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
Weight | 6.6 lb | 🏆 6.13 lb | 6.17 lb | not explicitly validated in final deck | 🏆 3.90 lb representative SKU | 11.40 lb
10G Uplinks | 🏆 2x10G + 2x1G | 2x1/10G + 2x1G | No | 2x10G | 1G or 10G SKU-dependent; not direct 12-port peer | 2x10G/1G
PoE Budget | 🏆 240W | 139W | 139W | 234W | 🏆 240W base / up to 480W with expansion | 🏆 240W
Stacking | No | 🏆 VSF up to 8 | Not confirmed | No evidence | No; modular expansion only | No
Environment | Campus / commercial | Campus / commercial | Campus / commercial | Campus / commercial | Rugged industrial / IP30 / DIN rail | 🏆 Rugged industrial / IP66-IP67
C9200CX wins campus breadth; Arista is the closest compact match; IE3500 Rugged and IE3500H split the industrial category

## Slide 5
Catalyst 9200CX Hardware Comparison
Core hardware and physical attributes
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
5
Category | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
CPU / Platform | UADP 2.0 Mini / 4-core ARM | ARM Cortex-A9 | ARM Cortex-A9 | Dual-core x86 | Industrial modular platform; CPU not direct compare target | Industrial heavy-duty CPU not direct compare target
DRAM / Flash | 4 GB / 8 GB | 4 GB / 16 GB | 4 GB / 16 GB corrected | 4 GB / 8 GB | 🏆 Series supports larger industrial memory / modular expansion context | 🏆 8 GB / 5.1 GB user storage
Packet Buffer | 6 MB | 🏆 12.38 MB | not specified | 2 MB | not explicitly normalized at series level | not officially published for exact SKU
MAC Table | 🏆 32K | 8K | 8K | Not clearly published | series-level values vary by SKU | 24K
Form Factor | Compact fanless 1U | Compact fanless 1U | Compact fanless 1U | Compact fanless 1U | 🏆 DIN-rail modular industrial | Heavy-duty wall-mount / field form factor
Physical Fit | 9.6 in depth | ~10 in class | ~10 in class | 9.8 in | 🏆 Most compact industrial footprint | largest / heaviest rugged package
For compact campus hardware, Arista is the closest structural peer; Aruba leads packet buffer; IE3500 Rugged leads modular industrial compactness

## Slide 6
PoE & Power Comparison
Critical for powered edge devices
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
6
Category | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
PoE Standard | 802.3at PoE+ | 802.3at PoE+ | 802.3at PoE+ | 802.3at PoE+ | 🏆 Industrial PoE / 4PPoE capable with expansion options | 🏆 PoE+ plus industrial 4PPoE-capable ports
PoE Budget | 🏆 240W | 139W | 139W | 234W | 🏆 240W base / 360W or 480W with expansion | 🏆 240W
Perpetual / Fast PoE | 🏆 Yes | No | No | Persistent PoE on reboot | industrial power resilience emphasis | not the main differentiator
Power Input | 315W AC internal | Internal 165W | Internal | External AC PSU options | 🏆 Dual DC 12–54V | 🏆 12–54V DC industrial
Best for High-Power / OT endpoints | Strong campus PoE headroom | Limited by 139W | Limited by 139W | Slightly lower total budget | 🏆 Highest industrial PoE density / modular growth | 🏆 Industrial high-power endpoint bias
Cisco wins campus PoE continuity; IE3500 Rugged wins modular industrial PoE density; IE3500H wins sealed DC industrial power architecture

## Slide 7
Security Features Comparison
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
7
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
MACsec | 🏆 AES-256 | No | No | Not fully substantiated | 🏆 MACsec-256 at series level | MACsec-128 on -E
DHCP Snooping / DAI / IPSG | 🏆 Yes / Yes / Yes | No / not confirmed / not confirmed | No / No / No | Not fully explicit in public source set | Industrial security feature set documented | Industrial security focus, not direct campus parity
Trust / Secure Boot | 🏆 Trust Anchor / Secure Boot | TPM integrated | TPM integrated | Security posture present, not equally explicit | Cyber Vision + SEA with Network Advantage | Secure boot / trust anchor class support
802.1X / TACACS / RADIUS | Yes | Yes | Yes | Expected campus support | Yes | Yes
Best security category | 🏆 Campus security depth | Limited | Basic | Good platform, less explicit public detail | 🏆 Industrial security / OT visibility bundle | Industrial security posture
Cisco is the campus-security winner; IE3500 Rugged adds the strongest explicit industrial security bundle; Aruba trails materially

## Slide 8
Software & Management Comparison
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
8
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
Operating System | IOS XE | AOS-CX | AOS-CX | EOS | IOS XE industrial | IOS XE industrial
Central Management | Catalyst Center / Meraki | Aruba Central | Aruba Central | CloudVision | DNA Center support | DNA Center support
Stacking / Consolidation | No | 🏆 VSF up to 8 | Not confirmed | No evidence | No; modular expansion only | No
Programmability | 🏆 RESTCONF / NETCONF / YANG / gNMI | REST API | REST API | EOS APIs / programmability | Cisco IOS XE automation family | Cisco IOS XE automation family
Telemetry | 🏆 Model-driven streaming telemetry | SNMP + sFlow | SNMP + sFlow | CloudVision telemetry | Industrial Cisco telemetry / OT visibility | Industrial IOS XE / DNA support
App Visibility | 🏆 NBAR2 / AVC | No | No | No NBAR equivalent | OT-focused visibility, different model | OT focus, not campus app vis
Aruba wins stacking; Arista wins EOS/CloudVision operations; Cisco wins campus programmability and app visibility; Rugged adds OT-oriented management value

## Slide 9
L2 / L3 Protocol Support
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
9
Protocol / Role | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
Static Routing | Yes | Yes | Yes | Expected but not fully enumerated | Yes | Yes
OSPF / EIGRP / IS-IS / RIP | 🏆 Explicitly documented | No / L2 only bias | No / L2 only bias | Not fully enumerated publicly | Industrial IOS XE family support | Industrial IOS XE family support
BGP / EVPN | Basic BGP on C9200CX | No | No | EVPN segmentation positioning | Series-level industrial routing / not positioned as EVPN compact peer | 🏆 BGP supported in reviewed IE set
PTP / Timing | 🏆 IEEE 1588v2 | Not a key differentiator | Not a key differentiator | Not directly substantiated | 🏆 TSN / frame-preemption / industrial timing posture | 🏆 IEEE 1588v2
Industrial Protocol Relevance | Campus platform | Campus platform | Campus platform | Campus platform | 🏆 Industrial redundancy / OT protocols / TSN posture | 🏆 OT / industrial protocol alignment
Cisco wins documented campus routing depth; IE3500 Rugged and IE3500H dominate OT protocol and timing relevance

## Slide 10
Reliability & Environmental Specifications
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
10
Criterion | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
MTBF | 🏆 Published 553K–704K hrs range | Not published | Not published | Not validated in deck | Not primary published takeaway in source set | Not the primary published takeaway in deck
Operating Temp | -5°C to 45°C | 0°C to 45°C | 0°C to 45°C | campus compact class | 🏆 -40°C to 75°C | 🏆 -40°C to 75°C
Humidity / Marine Margin | 5–90% non-condensing | 5–90% | 5–90% | Not positioned for marine extremes | Best protected industrial cabinet posture | 🏆 Best sealed harsh-environment posture
Ingress / Shock / Vibration | Not rugged rated | Not rugged rated | Not rugged rated | Not rugged rated | Shock / vibration / surge hardened, IP30 | 🏆 Industrial hardening / IP66-IP67
Marine Readiness | Not proven marine-certified | Not proven marine-certified | Not proven marine-certified | Not proven marine-certified | Good for protected industrial / cabinet use | 🏆 Closest practical harsh-environment fit
C9200CX is the only platform with clearly cited MTBF here; IE3500 Rugged and IE3500H are the real environmental contenders

## Slide 11
Telemetry & Monitoring Capabilities
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
11
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
SNMP / Syslog / LLDP | Yes | Yes | Yes | Yes | Yes | Yes
Flow Monitoring | 🏆 Flexible NetFlow | sFlow only | sFlow only | sFlow | Cisco OT visibility / monitoring stack | DNA support but not NetFlow-centric in deck
Streaming Telemetry | 🏆 Model-driven gRPC push | SNMP pull bias | SNMP pull bias | CloudVision telemetry | Industrial Cisco telemetry / OT visibility | Industrial Cisco automation family
YANG / Open APIs | 🏆 OpenConfig + native YANG | No | No | EOS APIs | IOS XE automation | IOS XE automation
Best observability category | 🏆 Cisco campus | Basic | Basic | Strong Arista telemetry ops | Strong OT visibility posture | Operational OT visibility, different goal
Cisco wins campus observability depth; Arista is the strongest compact alternative; IE3500 Rugged adds OT-oriented monitoring value

## Slide 12
Stacking, Scale, and Weight Impact
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
12
Aspect | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | IE3500 Rugged | Cisco IE3500H
Stacking Support | No | 🏆 VSF up to 8 | Not confirmed | No evidence in deck | No; modular expansion only | No
Mgmt entities at 2,500 | 2,500 units | 🏆 ~313 VSF stacks | 2,500 assumed | 2,500 units | Modular growth reduces node count per cabinet, not stacking | 2,500 rugged nodes
Weight Impact | Baseline 6.6 lb | 🏆 Best validated reduction | Moderate reduction | Not explicit in final deck | 🏆 Representative rugged SKU much lighter than IE3500H | Much heavier
Fleet-scale Ops Winner | No stacking | 🏆 Best management consolidation | Too basic | Closest compact alt, no stacking edge | Best modular industrial cabinet scaling | Environment-focused, not fleet simplification
Aruba CX 6100 is the fleet-scale weight/stacking winner; IE3500 Rugged is the better modular industrial scaling story; Cisco wins feature depth

## Slide 13
Recommendation Matrix
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
13
Priority | Winner | Reason
Best all-around campus access | 🏆 Cisco C9200CX | PoE, security, routing, telemetry, app visibility, and Cisco campus integration.
Closest clean compact substitute | 🏆 Arista CCS-710P-12 | Best 1:1 compact role alignment with fanless 12-port PoE and 2x10G uplinks.
Best protected industrial / cabinet deployment fit | 🏆 Cisco IE3500 Rugged Series | DIN-rail modular family, dual DC, RJ45, industrial hardening, TSN / OT posture.
Best sealed harsh-environment / field deployment fit | 🏆 Cisco IE-3500H-12P2MU2XE | IP66/IP67, DC, M12, industrial hardening, harsh-environment suitability.
Best weight / stacking compromise | 🏆 Aruba CX 6100 | Lowest validated weight and VSF stacking, but weaker security and telemetry.
Avoid when 10G / security / visibility matter | Aruba CX 6000 | Basic L2 access only; most constrained option in this study.

## Slide 14
Sources & Methodology
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
14
• Source decks merged: Cisco_C9200CX_Replacement_Analysis_Validated.pptx, C9200CX_vs_Arista_710P_Validated.pptx, C9200CX_vs_IE3500H_Validated.pptx.
• IE3500 Rugged Series was added from an official Cisco series-level fact set and is shown conservatively as a series column, not a forced 12-port 1:1 SKU match.
• Where one vendor had less explicit public detail than Cisco, the merged deck keeps the claim conservative instead of guessing.
• Winners are category-specific, not absolute; different platforms win different deployment conditions.
Source Set | Use In This Deck
Aruba validated deck | Used for weight, stacking, power, security, management, telemetry, recommendation logic
Arista validated deck | Used for 1:1 compact equivalence, efficiency, EOS / CloudVision, caveats
IE3500H validated deck | Used for ruggedness, industrial certifications, environmental fit, OT positioning
IE3500 Rugged official fact set | Used for DIN-rail modular industrial positioning, dual-DC power, RJ45, TSN, and industrial comparison points