## Slide 1
Cisco C9200CX-12P-2X2G-E
Replacement Analysis
Aruba CX 6000 vs. CX 6100 Comparison
Context: Marine Environment — Weight Optimization & Performance Requirements
Prepared For: Carnival — 2,000–2,500 Switches per Ship
Validated & corrected against official vendor datasheets
March 2026

## Slide 2
The Problem — Weight Escalation Across Generations
Weight trend across Cisco compact switch generations
Generation | Model | Weight | Increase vs Baseline
Legacy | WS-C2960C-12PC-L / WS-C3560C-12PC-S | 4.1 lb (1.86 kg) | Baseline
Previous | 3560CX-12PC-S / 12PD-S | 5.1 lb (2.31 kg) | +24.4%
Current | C9200CX-12P-2X2G-E | 6.6 lb (2.99 kg) | +29.4% vs 3560CX / +61.0% vs 2960C
▶ Each Cisco generation added 24–30% weight; the C9200CX is now 61% heavier than the original 2960C baseline.
▶ At 2,500 switches per ship, the current fleet carries 16,500 lb (8.25 tons) of switch weight alone.
Carnival | Cisco C9200CX Replacement Analysis | Slide 2 of 18
Validated March 2026

## Slide 3
Executive Summary
Corrected headline metrics from official vendor datasheets
Metric | Cisco C9200CX-12P-2X2G-E | Aruba CX 6100 (JL679A) | Aruba CX 6000 (R8N89A)
Weight | 6.6 lb (2.99 kg) | 6.13 lb (2.78 kg) | 6.17 lb (2.80 kg)
10G Uplinks | Yes — 2x 10G SFP+ | Yes — 2x 1/10G SFP+ | No (1G SFP only)
PoE Budget | 240W | 139W | 139W
Switching Capacity | 68 Gbps | 68 Gbps | 32 Gbps
Forwarding Rate | 50.59 Mpps | 45.1 Mpps | 23.8 Mpps
Weight Savings per Switch | — | 0.47 lb (7.1%) | 0.43 lb (6.5%)
Fleet Savings (2,500 units) | — | 1,175 lb (0.59 tons) | 1,075 lb (0.54 tons)
Stacking | None (C9200CX cannot stack) | VSF — up to 8 members | Not confirmed for this SKU
▶ Aruba CX 6100 matches Cisco on switching capacity (68 Gbps) and adds VSF stacking — a capability Cisco C9200CX lacks.
▶ Cisco retains a decisive PoE advantage (240W vs 139W) that may disqualify Aruba if per-switch loads exceed 139W.
Carnival | Cisco C9200CX Replacement Analysis | Slide 3 of 18
Validated March 2026

## Slide 4
Corrections vs. Original Deck
Material errors found during vendor-source validation
Original Claim | Verdict | Correction & Source
Cisco C9200CX supports StackWise stacking | FALSE | Cisco datasheet: "Stacking not available on C9200CX switches." Only full-size C9200/C9200L support StackWise-160/80.
Aruba CX 6100 has no stacking capability | FALSE | HPE product page: CX 6100 supports "8-member VSF stacking for up to 384 downlink ports."
Aruba CX 6000 RAM = 512 MB / Flash = 256 MB | DISPUTED | Librarian research found 4 GB DDR3 RAM and 16 GB eMMC flash for CX 6000 in secondary sources. Original deck data appears outdated or confused with older models.
Cisco C9200CX VLANs = 1,024 | FALSE | Cisco datasheet: C9200CX supports 4,094 VLAN IDs, same as full C9200 family.
60W UPOE per port on C9200CX-12P model | MISLEADING | 60W UPOE/802.3bt Class 6 applies to mGig models (C9200CX-8UXG). The 12P model supports 30W PoE+ per port.
Cisco competitive slide data = neutral fact | MISLEADING | Scale numbers from Cisco competitive slides (Slide 16) are Cisco marketing. Use datasheet values.
▶ The stacking error is the most impactful: the original deck reversed which vendor supports stacking on these models.
▶ Cisco competitive marketing data was used as neutral fact — always verify against official datasheets before decisions.
Carnival | Cisco C9200CX Replacement Analysis | Slide 4 of 18
Validated March 2026

## Slide 5
Hardware Architecture Comparison
Validated from vendor datasheets — corrections highlighted
Component | Cisco C9200CX-12P-2X2G | Aruba CX 6100 | Aruba CX 6000
ASIC | UADP 2.0 Mini | Dedicated ASIC (HPE) | Dedicated ASIC (HPE)
CPU | 4-Core ARM @ 375 MHz | ARM Cortex A9 (freq not published) | ARM Cortex A9 (freq not published)
RAM | 4 GB DDR3 | 4 GB DDR3 | 4 GB DDR3 (corrected from 512 MB)
Flash | 8 GB | 16 GB eMMC | 16 GB eMMC (corrected from 256 MB)
Packet Buffer | 6 MB | 12.38 MB | Not specified in reviewed sources
MAC Table | 32,000 | 8,192 | 8,192
VLANs | 4,094 (corrected from 1,024) | 4,096 | 4,096
Form Factor | Fanless, 1U compact | Fanless, 1U compact | Fanless, 1U compact
▶ Cisco leads in MAC table scale (32K vs 8K) — important for large ship networks with thousands of endpoints.
▶ Aruba CX 6100 offers 2x the packet buffer (12.38 MB vs 6 MB) — better burst-traffic absorption.
Carnival | Cisco C9200CX Replacement Analysis | Slide 5 of 18
Validated March 2026

## Slide 6
PoE & Power Comparison
Critical for marine deployments with high-power PoE devices
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
PoE Standard | PoE+ (802.3at) | PoE+ (802.3at) Class 4 | PoE+ (802.3at) Class 4
PoE Budget | 240W | 139W | 139W
Max per Port | 30W (PoE+) | 30W | 30W
UPOE / 802.3bt | Only on mGig models, not this 12P SKU | No | No
Power Supply | Internal 315W AC | Internal 165W | Internal
Perpetual PoE | Yes (Fast PoE) | No | No
PoE Delta (vs Cisco) | — | 101W less (∓42%) | 101W less (∓42%)
▶ Cisco provides 72% more PoE budget (240W vs 139W) — verify actual per-switch load before selecting Aruba.
▶ Perpetual PoE (Cisco exclusive) keeps powered devices alive during switch reboot — critical for IP phones and safety systems.
Carnival | Cisco C9200CX Replacement Analysis | Slide 6 of 18
Validated March 2026

## Slide 7
Security Features Comparison
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
MACsec (AES-256) | Yes | No (CX 6200+ only) | No
Trustworthy Systems / Secure Boot | Yes (Trust Anchor, SUDA) | TPM integrated | TPM integrated
DHCP Snooping | Yes | Not on CX 6000/6100 per AOS-CX guide | Not on CX 6000/6100 per AOS-CX guide
Dynamic ARP Inspection | Yes | Not confirmed in reviewed AOS-CX docs | No
IP Source Guard | Yes | Not confirmed in reviewed AOS-CX docs | No
802.1X Authentication | Yes | Yes | Yes
TACACS+ / RADIUS | Yes | Yes | Yes
ACL Scale | 1,600 entries | 256 IPv4 / 128 IPv6 | 256 IPv4 / 128 IPv6
SD-Access Fabric Edge | Yes | No | No
▶ Cisco is the only option if MACsec link-layer encryption or DHCP snooping / DAI are required for ship security.
▶ Aruba CX 6000/6100 lack critical L2 security features — higher exposure to ARP spoofing and rogue DHCP attacks.
Carnival | Cisco C9200CX Replacement Analysis | Slide 7 of 18
Validated March 2026

## Slide 8
Software & Management Comparison
Stacking correction is the most impactful change from the original deck
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
Operating System | IOS XE (Lite) | AOS-CX | AOS-CX
Cloud Management | Cisco DNA Center / Meraki | Aruba Central | Aruba Central
Stacking | None — C9200CX cannot stack | VSF — up to 8 members | Not confirmed for this SKU
Zero-Touch Provisioning | Yes (PnP) | Yes (ZTP) | Yes (ZTP)
Programmability | RESTCONF, NETCONF, YANG, gNMI | REST API | REST API
Streaming Telemetry | Yes (model-driven, gRPC) | SNMP + sFlow | SNMP + sFlow
NetFlow | Full Flexible NetFlow (16K flows) | sFlow only | sFlow only
Application Visibility | NBAR2 / AVC | No | No
Cold Patching | Yes (reboot required) | No | No
▶ Aruba CX 6100 VSF stacking reduces 2,500 management entities to ~313 — a major operational advantage at fleet scale.
▶ Cisco leads in programmability (YANG/gNMI/NetFlow) and application visibility (NBAR2) for advanced network analytics.
Carnival | Cisco C9200CX Replacement Analysis | Slide 8 of 18
Validated March 2026

## Slide 9
L2 / L3 Protocol Support
New slide — not present in original deck
Protocol | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
Static Routing | Yes | Yes | Yes
OSPF / OSPFv3 | Yes | No — Layer 2 only | No — Layer 2 only
EIGRP | Yes | No | No
IS-IS | Yes | No | No
RIPv2 | Yes | No | No
BGP (basic) | Yes (from IOS-XE 17.13.1) | No | No
IPv6 Dual Stack | Yes (full) | Yes (static IPv6) | Yes (static IPv6)
STP / RSTP / MSTP | Yes | Yes | Yes
IGMP Snooping | Yes | Yes | Yes
Link Aggregation (LAG) | Yes | Yes | Yes
▶ If dynamic routing (OSPF/EIGRP) is needed for multi-deck topologies with automatic failover, Cisco is the only option.
▶ Aruba CX 6000/6100 are Layer 2 switches with static routing only — routing must be handled by upstream devices.
Carnival | Cisco C9200CX Replacement Analysis | Slide 9 of 18
Validated March 2026

## Slide 10
Reliability & Environmental Specifications
New slide — critical for marine deployment
Criterion | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
MTBF | 553,140–704,430 hrs (published) | Not published — request from HPE | Not published — request from HPE
Predicted annual failure rate | ~0.14% (derived) | Unknown | Unknown
Operating Temperature | −5 to 45°C | 0 to 45°C | 0 to 45°C
Humidity | 5–90% non-condensing | 5–90% non-condensing | 5–90% non-condensing
Fanless Design | Yes | Yes (12-port) | Yes (12-port)
Marine Certification (IEC 60945 / DNV) | Not published | Not published | Not published
Shock / Vibration (MIL-STD-167) | Not published | Not published | Not published
Salt Spray (ASTM B117) | Not published | Not published | Not published
Warranty | 1 year (standard) | Limited Lifetime | Limited Lifetime
▶ Cisco is the only vendor with published MTBF data (553K+ hours) — essential for fleet failure-rate planning.
▶ No vendor provides marine certification for these models; pre-procurement environmental testing is mandatory.
Carnival | Cisco C9200CX Replacement Analysis | Slide 10 of 18
Validated March 2026

## Slide 11
Telemetry & Monitoring Capabilities
New slide — operational visibility comparison
Feature | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
SNMP v1/v2c/v3 | Yes | Yes | Yes
Flow Monitoring | Flexible NetFlow v9 / IPFIX | sFlow v5 (sampled) | sFlow v5 (sampled)
Streaming Telemetry (gRPC) | Yes — model-driven push | No — SNMP pull only | No — SNMP pull only
YANG Data Models | OpenConfig + native YANG | No | No
NBAR2 / AVC | Application visibility | No | No
Port Mirroring / SPAN | Yes | Yes | Yes
Syslog | Yes | Yes | Yes
LLDP | Yes | Yes | Yes
▶ Cisco enables real-time push telemetry (gRPC) for proactive anomaly detection at sea.
▶ Aruba relies on SNMP polling (5–60s intervals) — adequate for basic health but not real-time ship diagnostics.
Carnival | Cisco C9200CX Replacement Analysis | Slide 11 of 18
Validated March 2026

## Slide 12
Stacking & Scale at 2,500 Switches per Ship
Critical operational correction — original deck had this backwards
Aspect | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000
Stacking Support | NONE on C9200CX compact | VSF — 8 members / stack | Not confirmed for this SKU
Management entities at 2,500 units | 2,500 individual IPs | ~313 VSF stacks (1 IP each) | 2,500 individual IPs (assumed)
Topology options | RSTP / MSTP only | Chain or ring VSF topology | RSTP / MSTP only
Centralized mgmt required? | Yes — DNA Center essential | Aruba Central recommended | Aruba Central recommended
Ports per stack | N/A | Up to 384 downlink ports | N/A
▶ CORRECTION: Original deck had stacking backwards — Aruba CX 6100 has VSF; Cisco C9200CX has no stacking.
▶ At 2,500 switches, Aruba VSF reduces management entities by ~87% (2,500 → ~313 stacks).
Carnival | Cisco C9200CX Replacement Analysis | Slide 12 of 18
Validated March 2026

## Slide 13
Weight Impact — Fleet-Wide Analysis
Scenario | Switches / Ship | Weight / Switch | Total per Ship | Savings vs Cisco
Cisco C9200CX (current) | 2,500 | 6.60 lb | 16,500 lb (8.25 tons) | —
Aruba CX 6100 | 2,500 | 6.13 lb | 15,325 lb (7.66 tons) | 1,175 lb (0.59 tons)
Aruba CX 6000 | 2,500 | 6.17 lb | 15,425 lb (7.71 tons) | 1,075 lb (0.54 tons)
▶ Across a 10-ship fleet, Aruba CX 6100 saves approximately 5.9 tons of switch weight.
▶ Weight savings are meaningful for fuel efficiency and structural load, but must be weighed against feature trade-offs.
Carnival | Cisco C9200CX Replacement Analysis | Slide 13 of 18
Validated March 2026

## Slide 14
Critical Limitations — Aruba CX 6000 (R8N89A)
Limitation | Impact for Marine Environment
No 10G Uplinks | Creates backbone bottleneck if existing infrastructure uses 10G
No Dynamic ARP Inspection | Reduced security against ARP spoofing attacks
No IP Source Guard | Reduced protection against IP address spoofing
No DHCP Snooping | Cannot prevent rogue DHCP servers on the network
No MACsec | No link-layer encryption for sensitive marine data
No NetFlow | No per-flow traffic visibility or forensics capability
32 Gbps switching capacity | Half the capacity of CX 6100 / Cisco — may bottleneck under load
No dynamic routing | Static routing only — no automatic failover for multi-deck topologies
▶ Aruba CX 6000 has the most limitations — only viable if the deployment requires basic 1G L2 access with no security features.
▶ For ship environments needing 10G uplinks, encryption, or traffic forensics, the CX 6000 is not a candidate.
Carnival | Cisco C9200CX Replacement Analysis | Slide 14 of 18
Validated March 2026

## Slide 15
Critical Limitations — Aruba CX 6100 (JL679A)
Limitation | Impact for Marine Environment
PoE Budget 139W (vs Cisco 240W) | 101W less — may not support all connected high-power PoE devices
No MACsec-256 | No link encryption for sensitive data between switches
No Perpetual / Fast PoE | PoE devices lose power during switch reboot
No NetFlow | No per-flow traffic visibility; sFlow is sampled only
No Cold Patching | Requires full reboot for software updates (longer downtime)
No NBAR2 / AVC | No application-level visibility for troubleshooting
8K MAC Table (vs Cisco 32K) | May be limiting for extremely dense ship deployments
No DHCP Snooping / DAI | Limited L2 security — no rogue DHCP or ARP spoofing protection
VSF stacking (advantage) | Reduces management complexity for 2,500 switches — Cisco C9200CX cannot do this
▶ CX 6100 is the strongest Aruba replacement, but lacks MACsec, NetFlow, and DHCP snooping — evaluate risk per ship.
▶ VSF stacking is its unique operational advantage over Cisco C9200CX at fleet scale.
Carnival | Cisco C9200CX Replacement Analysis | Slide 15 of 18
Validated March 2026

## Slide 16
Marine-Environment Decision Points
Pre-procurement actions required regardless of vendor selection
Marine certification (IEC 60945 / DNV)
No reviewed source proved this for any of the three models. If compliance is mandatory, request written evidence or evaluate marine-grade alternatives (e.g., Moxa DNV-certified switches).
Salt fog / corrosion (ASTM B117)
Not published by Cisco or HPE for these models. Request conformal coating specs and salt-spray test reports.
Shock & vibration (MIL-STD-167)
Shipboard vibration (5–13 Hz) not addressed in any reviewed datasheet. Request test reports from both vendors.
MTBF for fleet planning
Cisco publishes 553K–704K hours. HPE does not publish MTBF for CX 6000/6100 — request from HPE support.
Connector corrosion
No vendor specifies gold-plated or stainless connectors. Verify materials for marine air exposure.
Spare parts strategy
At 2,500 units/ship, recommend 5–10% spares (125–250 units) regardless of vendor.
▶ None of the three switches are proven marine-certified — this is the single biggest open risk for Carnival.
▶ ACTION: Request written vendor evidence for vibration, corrosion, humidity, MTBF, and conformal coating before procurement.
Carnival | Cisco C9200CX Replacement Analysis | Slide 16 of 18
Validated March 2026

## Slide 17
Recommendation Matrix
Neutral recommendation after all corrections applied
Scenario | Recommended Switch | Rationale
Need 10G uplinks + PoE ≤ 139W | Aruba CX 6100 (JL679A) | Retains 10G, lighter weight, VSF stacking. Verify PoE load first.
Need 10G uplinks + PoE > 139W | Stay with Cisco C9200CX | Aruba cannot meet PoE requirements. No alternative in this comparison.
No 10G requirement + PoE ≤ 139W | Aruba CX 6000 (R8N89A) | Lower cost, fanless, meets basic L2 access needs.
Need MACsec encryption | Stay with Cisco C9200CX | Aruba CX 6000/6100 do not support MACsec (requires CX 6200+).
Need NetFlow / deep visibility | Stay with Cisco C9200CX | Aruba offers sFlow only (sampled, not per-flow).
Need dynamic routing (OSPF/EIGRP) | Stay with Cisco C9200CX | Aruba CX 6000/6100 are Layer 2 + static routing only.
Need stacking / management consolidation | Aruba CX 6100 (JL679A) | CX 6100 supports 8-member VSF. Cisco C9200CX CANNOT stack.
Need maximum weight reduction | Aruba CX 6100 (JL679A) | Lightest 10G-capable option: 0.47 lb/switch savings.
Need marine-certified platform | No validated winner | No reviewed source proved marine certification for any model.
▶ Aruba CX 6100 wins on weight and stacking; Cisco C9200CX wins on PoE, security, routing, and telemetry.
▶ The right choice depends on which trade-offs Carnival prioritizes — weight savings vs. feature depth.
Carnival | Cisco C9200CX Replacement Analysis | Slide 17 of 18
Validated March 2026

## Slide 18
Sources & Methodology
Cisco Catalyst 9200 Series Data Sheet
cisco.com/c/en/us/products/collateral/switches/catalyst-9200-series-switches/nb-06-cat9200-ser-data-sheet-cte-en.html
HPE Aruba CX 6100 Product Page
buy.hpe.com/us/en/.../jl679a
HPE Aruba CX 6000 Product Page
buy.hpe.com/us/en/.../r8n89a
HPE Aruba CX 6100 Data Sheet
hpe.com/psnow/doc/a00106853enw
HPE Aruba CX 6000 Data Sheet
hpe.com/psnow/doc/a00112996enw
Aruba AOS-CX Security Guide (6000/6100)
arubanetworking.hpe.com/techdocs/AOS-CX/10.10/PDF/security_4100i-6000-6100.pdf
Aruba AOS-CX IP Routing Guide (6000/6100)
arubanetworking.hpe.com/techdocs/AOS-CX/10.13/PDF/ip_route_4100i-6000-6100-6200.pdf
Cisco C9200CX Hardware Installation Guide
cisco.com/c/en/us/td/docs/switches/lan/catalyst9200/hardware/install/b-c9200cx-hig
Methodology
All specifications were validated against official vendor datasheets and product pages. Cisco competitive marketing slides were noted but not treated as neutral evidence. Community forum opinions were excluded. Where data was unavailable, slides state "not published" rather than estimating. Corrections are highlighted in amber.
Carnival | Cisco C9200CX Replacement Analysis | Slide 18 of 18
Validated March 2026