## Slide 1
Cisco C9200CX-12P-2X2G-E
vs. Arista CCS-710P-12
Compact Fanless 12-Port PoE Access Switch Comparison
Context: Same-format validated comparison using official Cisco and Arista sources
Prepared For: Carnival
Validated against official vendor product pages and datasheets
March 2026

## Slide 2
Executive Summary
Arista CCS-710P-12 is the closest clean 1:1 near-match found
Metric | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
Downlink Ports | 12x 1G PoE+ | 12x 1G PoE+
Uplinks | 2x 10G SFP+ + 2x 1G copper | 2x 10G SFP+
PoE Budget | 240W | 234W
Switching Capacity | 68 Gbps | 64 Gbps
Forwarding Rate | 50.59 Mpps | 95 Mpps
Form Factor | Compact, fanless, 1RU | Compact, fanless, 1RU
Power Input | 315W AC internal | 150W / 280W external AC PSU options
Management OS | Cisco IOS XE | Arista EOS
Telemetry | Model-driven telemetry, NetFlow | CloudVision telemetry, sFlow
▶ This is a much cleaner 1:1 comparison than IE3500: both are compact, fanless, 12-port PoE campus/edge switches with 10G uplinks.
▶ Cisco leads slightly on PoE budget and uplink flexibility; Arista leads on published throughput efficiency and power draw.
Carnival | C9200CX vs Arista 710P | Slide 2 of 13
Validated March 2026

## Slide 3
Why CCS-710P-12 Is the Correct Arista Equivalent
Selection Test | Result | Reason
12-port compact PoE intent | Match | Arista 710P-12 is a compact, fanless 12-port PoE campus switch.
10G uplinks | Match | Arista provides 2x 10G SFP+ uplinks, matching the core uplink intent.
Branch / access deployment | Match | Both target space-constrained access-layer deployments.
Fanless / quiet environments | Match | Both are designed for silent or quiet installation areas.
Exact uplink parity | Partial | Cisco adds 2x 1G copper uplinks; Arista uses SFP+ uplinks only.
▶ CCS-710P-12 is the best Arista near-match because it aligns on form factor, PoE access role, and compact deployment assumptions.
▶ Unlike the IE3500 comparison, no product-class mismatch is required here.
Carnival | C9200CX vs Arista 710P | Slide 3 of 13
Validated March 2026

## Slide 4
Ports, Uplinks, and Physical Interfaces
Parameter | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
Primary Ports | 12x 10/100/1000 RJ-45 PoE+ | 12x 10/100/1000 RJ-45 PoE+
10G Uplinks | 2x 10G SFP+ | 2x 10G SFP+
Additional Copper Uplinks | 2x 1G copper | None
Console / USB | Console + USB management ports | Console + USB
Mounting | Rack / wall / table | Rack / wall / ceiling / magnetic options
Acoustics | Fanless / silent | Fanless / silent
▶ Cisco’s only meaningful physical advantage is the extra 2x 1G copper uplinks.
▶ Arista counters with broader mounting flexibility for compact remote deployments.
Carnival | C9200CX vs Arista 710P | Slide 4 of 13
Validated March 2026

## Slide 5
PoE, Power, and Efficiency
Parameter | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
PoE Standard | IEEE 802.3at PoE+ | IEEE 802.3at PoE+
PoE Budget | 240W | 234W
Max PoE Delta | Baseline | -6W vs Cisco
Power Supply | 315W AC internal fixed PSU | 150W or 280W external AC PSU options
Switch Power (excluding PoE) | Higher system power footprint | 46W switching power published
Persistent / Fast PoE | Perpetual + Fast PoE | Persistent PoE on reboot
▶ Cisco has a small PoE headroom advantage (240W vs 234W), but the difference is operationally minor in many deployments.
▶ Arista’s published switching power is dramatically lower, making it more power-efficient for quiet edge environments.
Carnival | C9200CX vs Arista 710P | Slide 5 of 13
Validated March 2026

## Slide 6
Performance, Throughput, and Scale
Parameter | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
Switching Capacity | 68 Gbps | 64 Gbps
Packets / Second | 50.59 Mpps | 95 Mpps
System Memory | 4 GB DRAM | 4 GB system memory
Flash Storage | 8 GB flash | 8 GB flash
Packet Buffer | 6 MB | 2 MB
MAC Table | 32,000 | Not clearly published in fetched Arista source set
VLAN IDs | 4094 | Not explicitly confirmed in fetched 710P web page
▶ Cisco retains an advantage in packet buffer and documented L2 scale visibility.
▶ Arista publishes much higher packets-per-second throughput, suggesting a very efficient compact forwarding path.
Carnival | C9200CX vs Arista 710P | Slide 6 of 13
Validated March 2026

## Slide 7
Software, Management, and Telemetry
Feature | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
Operating System | Cisco IOS XE | Arista EOS
Central Management | Catalyst Center / Meraki monitoring | CloudVision
Streaming Telemetry | Model-driven telemetry | Real-time telemetry with CloudVision
Flow Visibility | Flexible NetFlow | sFlow
Programmability | NETCONF / RESTCONF / YANG | Extensive EOS APIs / programmability
In-Service Updates | Cold patching with reboot | In-service maintenance / upgrades highlighted
▶ Cisco has the richer published flow-monitoring story with Flexible NetFlow.
▶ Arista differentiates with EOS operational model consistency and CloudVision-centric telemetry workflows.
Carnival | C9200CX vs Arista 710P | Slide 7 of 13
Validated March 2026

## Slide 8
Security and Campus Feature Positioning
Feature | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
MACsec | AES-256 on C9200CX | Not directly confirmed in fetched 710P source set
802.1X | Yes | Campus security supported, but exact feature list not fully substantiated here
Trust Anchor / Secure Boot | Cisco Trust Anchor / Secure Boot | Arista security posture present, exact equivalent not fully confirmed here
Campus Segmentation | SD-Access support | VXLAN/EVPN segmentation highlighted
App Visibility | NBAR2 / AVC in Cisco family | Not positioned as NBAR equivalent
▶ Cisco’s campus-security and segmentation story is more explicitly documented in the reviewed source set.
▶ Arista is competitive on automation and segmentation architecture, but not all security details were equally explicit on the public pages reviewed.
Carnival | C9200CX vs Arista 710P | Slide 8 of 13
Validated March 2026

## Slide 9
L2 / L3 Protocol and Control-Plane Positioning
Capability | Cisco C9200CX-12P-2X2G-E | Arista CCS-710P-12
Layer 2 Campus Switching | Yes | Yes
Static Routing | Yes | Expected, but not fully enumerated in fetched web page
OSPF / EIGRP / IS-IS / RIP | Explicitly listed in Cisco 9200 datasheet family | Not fully enumerated in fetched 710P page
BGP / EVPN Positioning | Basic BGP on C9200CX from IOS-XE 17.13.1 | EVPN segmentation highlighted in 710P positioning
PTP | IEEE 1588v2 on C9200CX | Not directly substantiated in fetched 710P page
▶ Cisco publishes a more explicit compact-switch routing and timing feature list in the reviewed documentation.
▶ Arista’s public 710P positioning emphasizes campus segmentation, telemetry, and operational model over detailed per-protocol tables.
Carnival | C9200CX vs Arista 710P | Slide 9 of 13
Validated March 2026

## Slide 10
Deployment Fit: Branch, Quiet Spaces, and Edge Closets
Scenario | Best Fit | Why
Quiet rooms / conference / retail | Tie | Both are compact fanless switches designed for quiet deployment.
Need extra copper uplinks | Cisco | C9200CX adds 2x 1G copper uplinks.
Need lowest switching power draw | Arista | Arista publishes lower switching power consumption.
Need Cisco campus fabric alignment | Cisco | IOS XE, Catalyst Center, Trust Anchor, SD-Access alignment.
Need EOS / CloudVision operational model | Arista | Single EOS operational experience and Arista campus telemetry approach.
▶ This is a real head-to-head compact campus comparison: deployment fit is strong on both sides.
▶ The choice is less about hardware shape and more about operational ecosystem: Cisco campus stack vs Arista EOS/CloudVision.
Carnival | C9200CX vs Arista 710P | Slide 10 of 13
Validated March 2026

## Slide 11
Critical Caveats and Asymmetries
Topic | Finding
Uplink asymmetry | Cisco includes 2x 1G copper uplinks in addition to 2x 10G SFP+; Arista 710P-12 does not.
PoE budget asymmetry | Arista is 6W below Cisco (234W vs 240W) — usually minor, but verify high-density PoE loads.
Documentation asymmetry | Cisco datasheet exposes detailed L2/L3 scale tables; Arista 710P public pages emphasize operational and platform positioning more than full protocol tables.
Security detail asymmetry | Cisco MACsec-256 and Trust Anchor are explicit in reviewed sources; equivalent Arista security specifics were not equally explicit in the fetched 710P pages.
▶ The deck stays conservative where Arista public documentation was less explicit than Cisco’s datasheet tables.
▶ No unsupported feature was credited to Arista unless it appeared directly in the reviewed official material.
Carnival | C9200CX vs Arista 710P | Slide 11 of 13
Validated March 2026

## Slide 12
Recommendation Matrix
Priority | Recommended Platform | Why
Closest 1:1 compact hardware match | Arista CCS-710P-12 | 12x 1G PoE+, 2x 10G SFP+, compact fanless 1RU.
Maximum PoE headroom in this comparison | Cisco C9200CX-12P-2X2G-E | 240W vs 234W and richer uplink mix.
Best Cisco campus integration | Cisco C9200CX-12P-2X2G-E | Catalyst Center, SD-Access, Cisco Trust Anchor, IOS XE feature transparency.
Best EOS / Arista operational alignment | Arista CCS-710P-12 | CloudVision, EOS consistency, efficient compact edge design.
Lowest switching power draw | Arista CCS-710P-12 | Published switching power is substantially lower.
▶ If you want the cleanest Arista substitute for this exact Cisco compact switch, CCS-710P-12 is the right answer.
▶ Choose Cisco for tighter campus feature integration; choose Arista for EOS/CloudVision alignment and a cleaner low-power compact edge platform.
Carnival | C9200CX vs Arista 710P | Slide 12 of 13
Validated March 2026

## Slide 13
Sources & Methodology
Cisco Catalyst 9200 Series Data Sheet
cisco.com/c/en/us/products/collateral/switches/catalyst-9200-series-switches/nb-06-cat9200-ser-data-sheet-cte-en.html
Arista 710P Series Product Page
arista.com/en/products/710p-series
Arista 710P Datasheet (PDF)
arista.com/assets/data/pdf/Datasheets/CCS-710P-Datasheet.pdf
Arista 710XP Series Product Page
arista.com/en/products/710xp-series
Arista 710XP Datasheet
arista.com/assets/data/pdf/Datasheets/CCS-710XP-Datasheet.pdf
Methodology
This deck follows the same validated format as the prior Cisco comparison presentations. Arista CCS-710P-12 was selected as the closest official compact PoE near-match to C9200CX-12P-2X2G-E. Where Cisco documentation exposed more detailed scale data than Arista public pages, the deck marks Arista values conservatively rather than guessing.
Carnival | C9200CX vs Arista 710P | Slide 13 of 13
Validated March 2026