## Slide 1
Competitive Overview
C9200CX Competitive Comparison
Merged from validated Aruba, Arista, and IE3500H comparison decks
Prepared for: Carnival
March 2026
• Input decks merged: Aruba CX 6000/6100, Arista CCS-710P-12, and Cisco IE-3500H-12P2MU2XE.
• Reference model remains Cisco C9200CX-12P-2X2G-E across all tables.
• Winners are highlighted per category with green trophy markers.
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
1

## Slide 2
Key Technical Findings:
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
2
• Arista CCS-710P-12 is the closest true 1:1 compact competitor to C9200CX: same 12-port fanless PoE form factor with 2x10G SFP+ uplinks.
• Aruba CX 6100 is the lightest practical alternative with 10G-capable uplinks and VSF stacking, but it gives up major PoE, security, and telemetry features.
• Cisco IE-3500H-12P2MU2XE is not a campus peer; it is the ruggedized winner for harsh environments, with DC power, IP66/IP67, M12, and industrial hardening.
• Across feature depth, Cisco C9200CX remains the broadest all-around winner for campus access, while each competitor wins a narrower category.

## Slide 3
Cisco Catalyst 9200CX Switches
Competitive Landscape
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
3
Platform | Compared Model | Positioning | Key Differentiator
Cisco | C9200CX-12P-2X2G-E | Reference compact campus switch | 🏆 Best all-around campus feature set
Aruba | CX 6100 (JL679A) | Closest lightweight Aruba 10G option | Winner: stacking / weight
Aruba | CX 6000 (R8N89A) | Lower-end 1G-uplink option | Lacks 10G uplinks
Arista | CCS-710P-12 | Closest 1:1 compact Arista match | Winner: closest clean near-match
Cisco Industrial | IE-3500H-12P2MU2XE | Industrial / harsh-environment near-match | Winner: rugged / IP67 / DC

## Slide 4
Catalyst 9200CX Hardware Comparison
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
4
Category | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | Cisco IE3500H
Weight | 6.6 lb | 🏆 6.13 lb | 6.17 lb | not explicit in final deck | 11.40 lb
10G Uplinks | 🏆 2x10G SFP+ + 2x1G copper | 2x1/10G SFP+ + 2x1G | No | 2x10G SFP+ | 2x10G/1G SFP
PoE Budget | 🏆 240W | 139W | 139W | 234W | 🏆 240W
Form Factor | Compact fanless 1U | Compact fanless 1U | Compact fanless 1U | Compact fanless 1U | Industrial wall-mount heavy duty
Power Input | 315W AC internal | Internal 165W | Internal | External 150W/280W AC | 🏆 12-54V DC industrial
Packet Buffer | 6 MB | 🏆 12.38 MB | not specified | 2 MB | not officially published
Stacking | No | 🏆 VSF up to 8 | Not confirmed | No evidence in deck | No

## Slide 5
Catalyst 9200CX Hardware Comparison
Security / Operations / Environment
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
5
Category | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | Cisco IE3500H
MACsec | 🏆 AES-256 | No | No | Not fully substantiated | MACsec-128 on -E
NetFlow / Visibility | 🏆 Flexible NetFlow + telemetry | sFlow only | sFlow only | sFlow / CloudVision telemetry | DNA Center support
App Visibility | 🏆 NBAR2 / AVC | No | No | No NBAR equivalent | OT focus, not campus app vis
Campus Fabric | 🏆 SD-Access support | No | No | VXLAN/EVPN positioning | Industrial OT focus
Operating Temp | -5°C to 45°C | 0°C to 45°C | 0°C to 45°C | not emphasized as harsh-env | 🏆 -40°C to 75°C
Ingress / Ruggedness | No IP rating | Commercial campus | Commercial campus | Compact campus edge | 🏆 IP66 / IP67

## Slide 6
Catalyst 9200CX Scale Comparison
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
6
Scale Metric | Cisco C9200CX | Aruba CX 6100 | Aruba CX 6000 | Arista 710P-12 | Cisco IE3500H
MAC | 🏆 32K | 8K | 8K | Not clearly published | 24K
IPv4 / Host Routes | 14K total / 4K routing entries | 1K class | 1K class | Not explicitly published in source set | 🏆 7K IPv4
Forwarding Rate | 50.59 Mpps | 45.1 Mpps | 23.8 Mpps | 🏆 95 Mpps | 🏆 Line rate for all ports
Switching Capacity | 🏆 68 Gbps | 🏆 68 Gbps | 32 Gbps | 64 Gbps | Not officially published for exact SKU
Memory | 4 GB DRAM / 8 GB flash | 4 GB / 16 GB | 4 GB / 16 GB corrected | 4 GB / 8 GB | 🏆 8 GB / 5.1 GB user storage
C9200CX wins campus-scale balance; IE3500H wins rugged route scale; Arista wins compact forwarding efficiency

## Slide 7
Catalyst 9200CX Competitive Summary
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
7
Category | Winner | Reason
Closest 1:1 equivalent | 🏆 Arista CCS-710P-12 | Same compact fanless 12-port PoE role with 2x10G SFP+ uplinks.
Best all-around campus features | 🏆 Cisco C9200CX | PoE headroom, MACsec-256, NetFlow, app visibility, SD-Access, richer published L3/telemetry.
Best rugged / marine / OT fit | 🏆 Cisco IE-3500H-12P2MU2XE | IP66/IP67, DC power, M12, -40°C to 75°C, industrial hardening.
Best weight / stacking trade-off | 🏆 Aruba CX 6100 | Lowest validated weight and VSF stacking, but with major feature trade-offs.
Lowest-capability option | Aruba CX 6000 | Viable only if 1G uplinks and basic L2 access are acceptable.

## Slide 8
What We Need from the BU & PM
© 2026 OpenCode / Carnival internal working draft
Competitive Comparison
8
• Authoritative C9200CX MTBF and environmental guidance to compare fairly against rugged and campus competitors.
• Explicit public Cisco guidance for marine / hospitality deployments where weight, humidity, and non-standard mounting matter.
• A customer-ready positioning narrative for why C9200CX should be chosen over Aruba / Arista / IE3500 when requirements are mixed.
• Clear field guidance on when customers should move to IE3500H instead of forcing C9200CX into harsh-environment roles.
• Published competitive positioning on Arista 710P, since it is the cleanest compact non-Cisco near-match in this study.